## Slide 1
Equation of single variable
Seungpyo Hong
Flow Physics and Engineering Lab.
Department of Mechanical Engineering
POSTECH
Bisection method & Newton method

## Slide 2
Problem
Find the temperature which makes the vapor pressure of 0.5 atm.

## Slide 3
DO
ENDDO
Structure of the program
Choose the method. (1: Newton method, 2: Bisection method)
Initialize the variables. 1) For Newton method : initial approximation, tolerance, maximum number of iterations, possible range 2) For Bisection method : range of the solution, tolerance, maximum number of iterations
Go through each algorithm (Newton method)
If initial guess is beyond the prescribed possible range, set initial value as average of minimum and maximum values.
Get P(i) values until maximum iteration.
Take derivative of P(i) values (i.e. P_prime(i)) until tolerance of P value obtained above goes below tolerance (abs(P(i)) < 10E-4).
T(i+1) = T(i) – P(i)/P_prime(i)
Conditions

## Slide 4
Conditions
1) If T(i+1) and T(i) >= 1436 , adjust T(i) = T(i) – 60 (iterations can be reduced by choosing higher values)
2) If T(i+1) >= rangemax and T(i) >= 1436, adjust T(i) = T(i) – 60
If T(i+1) >= rangemax and T(i) < 1436, adjust T(i) = T(i) + 60
3) If T(i+1) <= rangemin, adjust T(i) = T(i) – 60
4) Two subroutines for calculating P and P_prime are inserted. When calculating P, if input variable is 0, adjust it to 0.1 in order to avoid error by calculating log(0.0).
Newton method
1436 K

## Slide 5
Bisection method
Until tolerance (abs(P) < 10E-4) and maximum number of iterations.

## Slide 6
Numerical example
Newton method |  | Bisection method | 
Initial approx | iter # | Range of sol | iter #
-3000 K | 8 | -3000 K ~ 7000 K | 18
0 K | 8 | 0 K ~ 700 K | 15
8000 K | 9 | -7300 K ~ 8000 K | 20
12000 K | 9 | -11300 K ~ 12000 K | 17
200 K | 4 | 200 K ~ 500 K | 6
500 K | 6 | 200 K ~ 500 K | 6
Sol 354.6875 K

## Slide 7
Conclusion
 | Newton method | Bisection method
Pros | High convergence rate (especially, when it comes to broad range) | Easy to implement (when it comes to narrow range)
Cons | Hard to implement (one has to think about exceptional case) Costly (use derivatives) | Low convergence rate (especially, when it comes to broad range)
Bisection method looks better if we know the range (narrow range) of the solution and Newton method is useful in general situation (broad range) with high convergence rate once it is implemented.