## Slide 1
Heat Conduction
Seungpyo Hong
Flow Physics and Engineering Lab.
Department of Mechanical Engineering
POSTECH
Numerical methods final term projects
Elliptic partial differential eqauation
with FDM and FEM

## Slide 2
Starting point
Unsteady
1D heat diffusion
Steady
2D heat diffusion
By using Jacobi iteration, write a program that solves this problem for given number of grid in different directions.
The number of Jacobi iterations? The solution varies less than 0.00005 at point (1, 0.5). Do it with (Nx, Ny) = (11, 11) and (21, 21).
Compare with Gauss-Seidel iteration and SOR.

## Slide 3
By using Jacobi iteration, write a program that solves this problem for given number of grid in different directions.
The number of Jacobi iterations? The solution varies less than 0.00005 at point (1, 0.5). Do it with (Nx, Ny) = (11, 11) and (21, 21).
Compare with Gauss-Seidel iteration and SOR.
Project # 1
Motivation and define the problems
FDM (for fluid) + FEM (for solid)
Project # 2
By using FEM, solve same problem with 3-node triangular element.
Repeat with 6-node triangular element.
Nice to have experience
on both numerical methods !

## Slide 4
Results of analytic solution

## Slide 5
Project #1
Heat Conduction Laplace Equation
with Finite Difference Method
Project #1

## Slide 6
PROGRAM Laplacefdm
Enter the number of nodes in x and y directions.
Allocation of the arrays
Choose the method to solve matrix.
(1: Direct inversion, 2: Jacobi, 3: Gauss-Seidel, 4: Successive over relaxation)
FDM code structure (1)
1. Form generic A matrix with central difference (penta diagonal matrix)
2. Modify A matrix by applying natural boundary conditions.
Project #1

## Slide 7
=
END PROGRAM Laplacefdm
FDM code structure (2)
3. Form B matrix by applying essential boundary conditions. (i =1)
4. Solve the matrix among selected procedure. - For direct inversion. Use matrix inversion subroutine in HW#3
- For others, iteration until difference of solutions between iteration is less than 0.00005 at point (1, 0.5).
c
c
Natural B.C.
Essential B.C.
5. Obtain top and bottom values with internal points and write the results.
Project #1

## Slide 8
Results of the solutions
Nx = 11 Ny = 11
Project #1
Absolute Error = 1.513738284471000e-003

## Slide 9
Results of the solutions
Nx = 21 Ny = 21
Project #1
Absolute Error = 3.059164619565652e-004

## Slide 10
Results of the solutions
Nx = 41 Ny = 41
Project #1
Absolute Error = 6.751667681226800e-005

## Slide 11
Error analysis
Project #1
Chart: Grid convergence test for FDM
| 11 | 21 | 41
log(error) | -2.8199 | -3.5004 | -4.1706
Recall Log(4) = 0.602059913

## Slide 12
Iterative solution methods
Project #1

## Slide 13
Project #1
Number of iterations vs iteration method
Method | 11 | 21
Point Jacobi | 352 | 1024
Gauss-Seidel | 218 | 667
SOR | 46 | 176

## Slide 14
Project #2
Heat Conduction Laplace Equation
with Finite Element Method
Project #2

## Slide 15
Weak formulation (1)
Project #2

## Slide 16
Weak formulation (2)
Project #2

## Slide 17
Calculate stiffness matrix (1)
Project #2
For three node element (3 by 3)
For six node elemement (6 by 6)
(by using Gauss quadrature)

## Slide 18
Calculate stiffness matrix (2)
Project #2

## Slide 19
Assemble global matrix
Project #2
c
=

## Slide 20
Give boundary conditions
Project #2

## Slide 21
PROGRAM Laplacefem
END PROGRAM Laplacefem
Enter the element type. (1: linear, 2: quadratic)
Choose the number of element on one side.
Allocation of the arrays
FEM code structure
Linear element
1. Give number and element connectivity.
2. Calculate stiffness matrix 3. Assemble the matrix
4. Give boundary condition
5. Matrix inversion
Quadratic element
1. Give number and element connectivity.
2. Calculate stiffness matrix
(with Jacobian and Gauss quadrature) 3. Assemble the matrix
4. Give boundary condition
5. Matrix inversion
Project #2
Write the results

## Slide 22
Results
Test case with 8 3node elements
No error at (1,0.5)

## Slide 23
Results
Test case with 200 3node elements
No error at (1,0.5)

## Slide 24
Results
Test case with 8 6node elements
Still struggling, one possiblity is the number of meshes