## Slide 1
    Numerical
    Analysis
    for Materials
20130528
Dept. of Materials Science and Engineering
Cheolhee Han
Homework No.8

## Slide 2
    01 Algorithm
    Numerical Solution of PDE(Forward Difference Method)
Numerical Methods
Forward Difference Method(Explicit Method)
Implicit Method
Crank-Nicolson Method
Concentration
A
B
x
0
0.01
0.05
A
double dt = 1;
double dx = 2.5*pow(10, -6);
double D = diff_coeff(T);
double lambda = D*dt / pow(dx, 2);

## Slide 3
    02 Calculation Results
    Distance vs Concentration
Chart: T=1173K(λ=0.019)
Chart: T=1273K(λ=0.063)
Chart: T=1373K(λ=0.174)
Chart: T=1473K(λ=0.419)

## Slide 4
    02 Calculation Results
    Injection Time Dependence
Chart: Injection Distance vs Time0.5
| 10 | 22.360679774997898 | 31.622776601683793 | 38.729833462074168 | 44.721359549995796 | 50 | 54.772255750516614 | 59.16079783099616 | 63.245553203367585 | 67.082039324993687 | 70.710678118654755
1173K | 3.3998e-06 | 7.3819e-06 | 1.0452e-05 | 1.2788e-05 | 1.4762e-05 | 1.6516e-05 | 1.8085e-05 | 1.9529e-05 | 2.0882e-05 | 2.214e-05 | 2.3343e-05
1273K | 1.3404e-05 | 1.8936e-05 | 2.3181e-05 | 2.6763e-05 | 2.9911e-05 | 3.2767e-05 | 3.5394e-05 | 3.7837e-05 | 4.0128e-05 | 4.23e-05
1373K | 2.2252e-05 | 3.1463e-05 | 3.8527e-05 | 4.448e-05 | 4.9727e-05 | 5.4473e-05 | 5.8837e-05 | 6.2895e-05 | 6.6709e-05 | 7.0309e-05
1473K | 3.4524e-05 | 4.8808e-05 | 5.9765e-05 | 6.9007e-05 | 7.7106e-05 | 8.4308e-05 | 9.0692e-05 | 9.6269e-05 | 0.00010107 | 0.00010513
Target(0.03)을 기준으로 전 후 값을 찾아 값을 구함(linear 가정)

## Slide 5
    02 Calculation Results
    Injection Temperature Dependence

## Slide 6
    03 Conclusion
    Activation Energy & Conclusion
Activation Energy
Injection Temperature Dependence 에서 구한 추세선의 기울기 평균: -8839.17
Slope = -Q/2R 이었으므로 Q는 -8839.17 * 2 * 8.3144598 = 146985.8473J
주어진 값 147723J과의 상대오차 = 0.499%
Answers
FDM을 통해 Diffusion proces를 이해하고 concentration과 distance 사이의 관계를 plot할 수 있다.
Injection time/temperature과 injection distance 사이의 관계를 확인할 수 있다.
Activation Energy를 계산하여 주어진 값과 비교할 수 있으며 그 오차는 0.499%이다..
Target value(0.03) 조건을 찾을 때 linear approximation 대신 cubic spline이나 다양한 보간법을 사용해서 오차를 줄일 수 있지 않을까?