## Slide 1
Numerical Method
HW #8
20200552 이형진

## Slide 2
HW8) Partial Differential Equation
[Problem]

## Slide 3
HW8) Partial Differential Equation
[Background]
FDM of Parabolic Problems
FDM: Finite Difference Method, 도함수들을 유한제차분으로 근사하여, 연립방정식으로 미분방정식을 해결
[Setting]
Δx = 0.000002m
Δt = 0.5s
L = 0.0004m
Checked when t = 100s, 200s, 400s, 800s, 1600s
<Initial Value>
C = 0.05 when x = 0
dC/dt = 0 when x = L
C = 0.01 when t = 0

## Slide 4
HW8) Partial Differential Equation
<1173K>
λ = 0.0157
<1273K>
λ = 0.0514
[Composition Result at T=1173K, 1273K, 1373K, 1473K]
<1373K>
λ = 0.1418
<1473K>
λ = 0.3404

## Slide 5
HW8) Partial Differential Equation
Chart: sqrt(time)
| 10 | 14.142135623730951 | 20 | 28.284271247461902 | 40
1473K | 15.75 | 22.25 | 31.46 | 44.45 | 62.9
1373K | 10.16 | 14.36 | 20.29 | 28.7 | 40.61
1273K | 6.12 | 8.67 | 12.22 | 17.3 | 24.48
1173K | 3.42 | 4.83 | 6.78 | 9.57 | 13.53
Injection Distance ∝

## Slide 6
HW8) Partial Differential Equation
Chart: 1/T
| 8.5251491901108269E-4 | 7.855459544383347E-4 | 7.2833211944646763E-4 | 6.7888662593346908E-4
100s | 1.2296 | 1.8116 | 2.3185 | 2.7568
200s | 1.5748 | 2.1599 | 2.6644 | 3.1023
400s | 1.914 | 2.5031 | 3.0101 | 3.4487
800s | 2.2586 | 2.8507 | 3.3569 | 3.7944
1600s | 2.6049 | 3.1979 | 3.704 | 4.1415
Injection Distance ∝

## Slide 7
HW8) Partial Differential Equation
Injection Distance ∝
Injection Distance ∝
(b)에서의 그래프의 기울기 = -Q/2R = -8826.48 (평균)
Q = 146766.7 J
Calculated Value (J) | 146766.7
Real Value (J) | 147723
Error (%) | 0.64%